## Slide 1
Revision complete | Main topic heading
 | Selection of materials or components
 | Forces and stresses
 | Ecological and social footprint
 | Sources and origins
 | Using and working with materials
 | Stock forms, types and sizes
 | Scales of production
 | Specialist techniques and processes
 | Surface treatments and finishes
 | Investigation, primary and secondary data
 | Environmental, social and economic challenge
 | The work of others
 | Design strategies
 | Communication of design ideas
 | Prototype development
 | Selection of materials and components
 | Tolerances
 | Materials management
 | Specialist tools and equipment
 | Specialist techniques and processes

## Slide 2
Selection of materials or components | 
Key Points | Key Words
Many factors affect the functionality of textile products Choosing fabrics and components carefully can protect the environment and the well-being of people who make them Styles of clothing are often dictated by social and cultural factors | Bulk buying When materials or products are bought in large quantities they usually cost less per unit than buying just a few. This is because the costs of setting up the manufacturing are the same no matter how many are made.
Forces and stresses | 
Key Points | Key Words
There are five main types of force that can act upon any object or structure: tension, compression, shear, bending and torsion Some materials are better at resisting certain forces Materials can be reinforced and stiffened in order to resist certain forces | 
Ecological and social footprint | 
Key Points | Key Words
Deforestation is where large areas of trees are cut down, often due to mining, drilling , farming, or logging Mining can damage the environment and causes related problems for local people Farming uses about 70 per cent of the worlds useable water supply, which means less is available for other purposes. | Mining The extraction of minerals and metals from ground Drilling The process of making a hole in the Earth’s surface, usually to extract liquids or gas Farming The use of land for growing crops or keeping animals for food Eutrophication Excessive nutrients in a body of water, often caused by fertilisers Deforestation Large areas of trees cut down, often due to mining, drilling, farming or logging.

## Slide 3
Sources and origins | 
Key Points | Key Words
Cotton is a natural cellulose fibre that comes from the ripened seeds found inside bolls, from s bushy plant grown in tropical parts of the world Wool hair fibre sheared from a sheep or other fleecy animal. It is sent to a mill to be cleaned and scoured to remove grease and dirt, graded and sorted for quality, carding and combing to straighten the fibres and then spinning to make yarn. Silk is a protein fibre that comes from the cocoon of the silk caterpillar. The cocoon is dropped in boiling water and the silk filaments are unwound. Synthetic fibres are manufactured from oil- or coal- based chemicals that made into a polymer and melted to make a solution that is spun into continuous lengths of fibre Fibres are usually twisted together to make a yarn before they are made into a fabric. | 
Using and working with materials | 
Key Points | Key Words
Fabric must be matched with their properties and the requirements of the end product The type of fabric and appearance must be considered when choosing seams to use on a product The type of fabric and appearance must be considered when choosing seams to use on a product Shaping is used to give from and ease to a product Fibre and fabric properties can be modified for specialist applications | 
Stock forms, types and sizes | 
Key Points | Key Words
Yarns are made by plying two or more single yarns together It is important to know the width of a fabric when calculating quantities Trimmings and components are used for functional and decorative purposes | 

## Slide 4
Scales of production | 
Key Points | Key Words
Production can be categorised by the amount that is produced – this is called scales of production One- off production is chosen wen a single product is made Batch production is chosen when several of the same product are required before the design of the product needs to change Mass production is used when a large number of the same product are needed. It uses a well-organised production line Continuous production is good when the cost of starting the business and running the necessary equipment is high. The product needs a constant and steady demand. | Prototype An early sample, model, or release of a product built to test a concept or process Batch production When a limited number of the same product is made during a particular period of time Down time When a machine has stopped working and no products are being made. This could be for maintenance, because the machine has developed a fault, or the time taken to set the machine up for a new operation One-off production When just one complete product is produced Mass production Manufacturing in large quantities over a long period of time. This typically uses a production line Continuous production Runs constantly and is highly automated
Specialist techniques and processes | 
Key Points | Key Words
Pattern templates are developed from basic blocks in standardised sizes Many layers of fabric are cut out at once in commercial manufacture Commercial machinists usually work on specific sections of a product before passing it on to someone else who makes a different part of the product Computer control is used in industry to carry out identical and repetitive processes Quality control is am important part of manufacture to make sure that products are made to the quality specified in the manufacturing and product specifications. | 

## Slide 5
Surface treatments and finishes | 
Key Points | Key Words
Colour and pattern can be applied to fabric with dyeing and printing Chemical finishes can improve the performance characteristics of fabrics Stain and water-repellent finishes can keep products cleaner for longer | 
Investigation, primary and secondary data | 
Key Points | Key Words
Market research is carried out to gain an understanding of the target market for a product Interviews, questionnaires and focus groups are examples of primary research methods that use questions to find out what people are thinking A designer must take into account human factors when designing products, including physiological, psychological and sociological factors Anthropometrics is a record of human measurements that is very useful to anyone who intends to produce something that will be used by a large number of people A design brief describes the problem or situation that needs a design solution When you have completed initial research, you will have answers to many of the questions that you set yourself at the beginning of your project. These answers will influence ideas for you project, and you may not have all the answers. Further ongoing research may be needed during the design process A design specification contains all the information necessary to make the product As designers work through projects and make attempts to solve the problems, new problems may be found which change how the design brief is understood It further research and testing finds aspects that are critical to the success of the project, and without which the project would not work, changes in the design brief should be made. | Primary research Any type of research where you collect new information yourself (for example, through interviews, surveys or observations) Secondary research Gathering existing data that has already been produced (for example, using books, newspapers, magazines or the internet) Human factors Considerations that are concerned with people Ergonomics The relationship between people and products, and how they use and interact with them

## Slide 6
Environmental, social and economic challenge | 
Key Points | Key Words
Designers have the responsibility for choosing their materials and processes carefully, so as to have the least impact on the environment and vulnerable communities Deforestation can be avoided with the correct management of forests. Designers can choose to use FSC materials, which are wood, paper or board that has been taken from sustainable and well-managed forests Fair trade products have been made by communities who have been given a fair price for their goods. This offers some protection to these communities against exploitation. | Deforestation Large areas of trees cut down, often due to mining, drilling, farming or logging FSC The forest stewardship council Fairtrade mark The mark that identifies products that have been bought fairly
Design Strategies | 
Key Points | Key Words
Negative feedback is used in a system to hold an output at a fixed level, whereas positive feedback is used to make sure that something happens by magnifying a small change Hunting is when a system is trying to achieve something but keeps overshooting the target and tries to correct but overshoots again Flowcharts are used to show or plan sequences Complex systems can be split into sub-systems, which simplifies both designing and testing When designing systems, look at the opportunities that incorporating feedback would offer Modelling, whether actual or virtual, allows the system to eb tested before committing to manufacture | 
The work of others | 
Key Points | Key Words
Design movements are particular styles with a group of people. Within these design movements these were key influential designers. William Morris is famous for his furniture & wallpaper designs Alexander McQueen, Coco Chanel, Vivienne Westwood and Mary Quant were all fashion designers of diff times and styles. Braun, Dyson, Apple and Alessi are successful companies that still design products today | Design movement A style of design particularly popular with a group of people or within a period of time

## Slide 7
Communication of design ideas | 
Key Points | Key Words
Freehand, isometric and perspective sketching techniques are used to communicate design intent A rage of enhancement and rendering techniques can improve the communication of design intent | Free hand sketching Drawing done without the use of rulers or drawing aids. It is a way that a designer can quickly express thoughts and ideas Isometric drawing Means equal measure.it is a technique of presenting a design sketch in three dimensions Rendering The addition of colour, or textures, to enhance a sketch to better communicate design intent
Prototype development | 
Key Points | Key Words
Prototypes are used to test and modify design ideas Prototypes can e physical or virtual models Prototypes often form part of the agreement between a manufacturer and client Prototypes can be used to show innovative designs and check their viability Rapid prototyping allows small numbers of specialised products to be made economically A rigorous testing and evaluation scheme is important to decide if the product design will be successful | 
Selection of materials and components | 
Key Points | Key Words
The function of the product must be considered when choosing fabrics and components There is a huge variety of fabrics and components available to suit all budgets Fabrics and components can be bought in many different outlets. | 

## Slide 8
Tolerances | 
Key Points | Key Words
Tolerances are the acceptable range of size a product or part can be Tolerances are shown as + or – the acceptable dimension Tolerances are important where components fit together The smaller the tolerance the more accurate the product More accurate tolerances will make a more consistent product, but may also increase manufacturing costs | 
Materials management | 
Key Points | Key Words
Fabric layouts need to use fabric as economically as possible to reduce costs Layouts need to be planned carefully to make sure that any pattern is used effectively Seam and hem allowances need to eb included on pattern templates It is important to place the straight grain line of the pattern template parallel to the fabric selvedge | 
Specialist tools and equipment | 
Key Points | Key Words
Sewing machines can be used to perform many different functions in the making and decorating of textile products It is important to use the most appropriate tool for the task in order to achieve a high-quality finish Care should be taken to use tools and equipment efficiently and correctly | 
Specialist techniques and processes | 
Key Points | Key Words
Cutting fabric accurately on the correct grain is important for the appearance and performance of the product Pressing work as you go along can help achieve a good finish The choice of construction and decorative techniques affects the appearance and functioning of the product Checking prints for accuracy will ensure that the fabric is aesthetically pleasing |